# Basic Parts of a Custom Shape
## Examine Markup of Predefined Shape ‘Right Triangle’
Start a new Draw document and insert the shape ‘Right Triangle’ at position x = 50 mm, y = 20 mm with size width = 40 mm and height = 60 mm. The shape belongs to the set ‘Basic Shapes’. In case you work with the packed file format ‘.odg’, enter the package and open the file content.xml in an editor. In case you work with the flat file format ‘.fodg’, open it directly in an editor. Search for the element <draw:custom-shape>. You should see something similar to the following markup
<draw:custom-shape draw:style-name="gr1"
        draw:text-style-name="P1"
        draw:layer="layout"
        svg:width="4cm"
        svg:height="6cm"
        svg:x="6cm"
        svg:y="3cm">
    <text:p/>
    <draw:enhanced-geometry … />
</draw:custom-shape>
### Common Parts
The attributes of a <draw:custom-shape> element are similar to other shape types.
draw:style-name="gr1"	The shape uses the graphic properties which are contained in a style with name ‘gr1’. Those determine the fill style and stroke width, for example.
draw:text-style-name="P1"	The shape uses for the text in the shape the paragraph properties which are contained in a style with name ‘P1’. Your shape has no text. That can be seen by the empty element <text:p/>.
draw:layer="layout"	The shape is placed on the layer ‘layout’. Layers exist only in Draw and Impress. It is irrelevant for this tutorial.
svg:width="4cm" svg:height="6cm"	The attributes svg:width and svg:height determine the size of the shape. LibreOffice has an internal precision of 1/100 mm. Because of rounding errors between non-metric system (inch, point) and metric system (mm, cm) the values are sometimes by 1 or 2 hundredth millimeter too small or too large. Don’t worry about it.
svg:x="6cm" svg:y="3cm"	The attributes svg:x and svg:y determine the position of the shape. For details see section Error: Reference source not found.
In case the shape is rotated or sheared, there will be a draw:transform attribute instead of svg:width, svg:height and svg:x, svg:y.
The part which is specific for a custom shape is the element <draw:enhanced-geometry … />
### First Look at Element <draw:enhanced-geometry>
<draw:enhanced-geometry
    svg:viewBox="0 0 21600 21600"
    draw:glue-points="0 0 0 10800 0 21600 10800 21600 21600 21600 10800 10800"
    draw:text-areas="1900 12700 12700 19700"
    draw:type="right-triangle"
    draw:enhanced-path="M 0 0 L 21600 21600 0 21600 0 0 Z N"
/>
draw:type="right-triangle"	LibreOffice uses this attribute to decide, how to treat the shape in import from and export to Microsoft file formats. The ODF standard allows to omit this attribute, but LibreOffice needs it to decide how to handle the shape.
For your own shapes you use always draw:type="non-primitive".
draw:enhanced-path="…"	The drawing of the shape consists of geometric elements like lines, curves or circles. The draw:enhanced-path attribute contains the definition of the drawing. It is a sequence of commands and coordinates of points. This attribute is mandatory.
svg:viewBox="0 0 21600 21600"	The definitions of the geometric elements use a local, unit-less coordinate system for the points. As usual in 2D computer graphics the x‑axis points right and the y‑axis points down. This attribute is mandatory.
Find more about this attribute in section Error: Reference source not found.
draw:glue-points="…"	You know, that each shape has four default glue points and the user can add own glue points in addition. Custom shapes may have additional, shape specific glue points. They are listed in this attribute. It is optional.
draw:text-areas="…"	The rectangular area into which text writing is possible can be explicitly set. The values determine the left, top, right and bottom edge of this area. This attribute is optional. If it is missing, the entire custom shape is used.
In case the shape is mirrored, there will be draw:mirror-horizontal and draw:mirror-vertical attributes.