THE WEDGIE SLED

Overview

INTRODUCTION

My sled is made of Corian. I like the stability of the material but you can make yours out of MDF, Melamine or whatever you choose.

The fences shown on the following pages are made to be reversible for both left and right tilt table saws.
The dimensions are not critical. The height of this fence works well with a segment thickness of 3/4-inch or less. Thicker segments will require a taller fence appropriate to the material.
The upper fence B must be ripped absolutely parallel and the edges of both fences must be flat.
All hardware is 1/4 inch. The hold down clamps are best positioned back from the blades as shown.
The distance between the fences determine the maximum width of segment material you can use; adjust as necessary.

A total of 82 Wedgie configurations are available from . www.segeasy.com

This Wedgie sled was made by Kendall Westbrook. He made the fences taller to accommodate the large segments he uses in his vessels. He also modified the distances between the fences for wider strip material.
Making the fences absolutely parallel took some effort. One particularly helpful addition was the handle block at the bottom.
With a wider fence separation, a spacer strip may be necessary to correctly locate a higher segment Wedgie such as the 48 as shown.
Of course the spacer strip must be perfectly parallel.
The Wedgie method is forgiving and you can modify the sled to accommodate what you need.

THE SLED BASE AND FENCES

From the backside:
1 In.

Cut a groove all the way through with a 1/4 inch straight router bit. You might have to make 2-3 passes.

Cut a 3/16 inch deep retaining groove with a 3/4 inch flat bottom router bit.

Note: This layout works for both left- and right-tilt saws.

The fences will work on either a right- or left-tilt tablesaw. For a left-tilt saw, simply flip them over.

Use a ¼” router bit and an appropriate jig to make the slots.

The holes for the hold-down clamps are not dimensioned, as these clamps vary considerably.

Take care when ripping the fences. Fence B must be absolutely parallel.

THE SLIDER/GUIDE FOR THE BASE

I like a simple wood track/GUIDE for sleds. The problem with any track is a dependable, easy adjustment system.

For the sled to perform well every time you use it, a track slide that is easy to adjust is a must. Even the slightest lateral movement in the sled will translate into an angle change in the segment.
This slide has an adjustment screw in each end that can be immediately accessed and adjusted with the sled in place, no guesswork. The screw serves as a wedge to spread the slide end apart in the saw slot. It is deceivingly simple and dependable.

In the photo at right, the screw is shown excessively deep in the slot.

Cut a strip of maple, oak or poplar that will slide easily in the saw slot. Make the thickness a little less than the slot depth. The length can be the same as the sled or a slightly longer.

Mark the center of each end and using a 1/4 inch Forstner bit, drill a 1/4 inch deep hole, in each end.

With a 3/32 bit, drill to a depth of 5/8 inch from each end.

Cut a slot down the center of the slide about 1-1/2 inches long. Be certain to center this cut on the center of the sliide.

Install a no 4 brass wood screw flush with the end of the
strip. It will be used later to correctly adjust the fit in the saw slot. [see photo].

ASSEMBLING THE BASE AND BLADE GUIDE
Install a no 4 brass wood screw flush with the end of the strip. It will be adjusted later to correctly fit in the saw slot.
Cut a slot down the center of the slide about 1-1/2 inches long.

Measure from the outside of the blade to the inside of the saw slot.

The placement of the track does not have to be perfect. A regular tape measure is fine.

Transfer this measurement to the Wedgie sled. This allows a saw blade's width for trimming of the sled.

With double stick tape the full length of the slide, mount with the inside of the slide to the marks.

Drill, tap and countersink for a 1/4 inch flathead machine screw.

Add Anti-friction UHMW tape to the underside of the sled.

The tape serves also to elevate the sled slightly to help match top of the zero clearance strip.

Crank the saw blade all of the way down and put the sled in place.
Adjust each end of the track slide until there is no lateral play but still has easy sled movement.

Making a Zero Clearance Ramp Strip
PREVENTING SEGMENT JAMS AND KICKBACK

Start out by cutting several strips about 1 inch wide with a 45 degree bevel on one edge. As the strips are consumable it makes sense while you are doing it to make several. Do not even think of cutting segments without a zero clearance strip.

With the Wedgie Sled in place as shown, stick down the ramp strip to an MDF plate saw insert. Make sure the strip is against the sled.

Drill, tap and countersink holes for a 10-24 machine screw through the insert and ramp strip. Do this on both ends.

The ramp strip must not pro­trude above the sled. If it does, sand down until level or slightly below.

With the Wedgie sled in place, turn on the saw and bring the blade up through the ramp strip until at the optimum cutting height. Optimum cutting height of the blade is typically 1/8” above the wood being cut.
Page 6

Take care to not extend the blade above this height as we want zero clearance in front of the blade as well as the side.

The ramp encourages the segments to fall away from the blade. They can pile up and encroach on the blade. Before this happens, stop the saw and move them out of the way. This picture is without the blade guard, simply for clarity .

Never cut segments without the guard.

SEGMENT CHOICES
CIRCLE [°]	SEGMENTS	SEGMENT ANGLE	SEGMENT ½ ANGLE
360	2	180	90
360	3	120	60
360	4	90	45
360	5	72	36
360	6	60	30
360	8	45	22.5
360	9	40	20
360	10	36	18
360	12	30	15
360	15	24	12
360	16	22.5	11.25
360	18	20	10
360	20	18	9
360	24	15	7.5
360	30	12	6
360	32	11.25	5.625

Simplified wedgie sled

https://www.youtube.com/watch?v=AdF7sKMKRR0

Before starting this project, watch the video under the title above

Create a basic sled with a T-track on the top and a miter runner on the bottom.
Before we go any further, use the router table to make a dado for the T-track. Install the T-track, using screws or epoxy, or both. Once the runner is in place, make a pass on the table saw to make the edge ZERO CLEARANCE.

Drill 2 holes to anchor the WEDGIES TO THE SLED. They should be on a line perpendicular to the BLADE AND ZERO CLEARANCE EDGE. Use 1/4”-20 threaded inserts to hold the WEDGIES TO THE SLED, and anchor them using matching knobs.

WEDGIES WILL BE MADE next.
Each WEDGIE will have 2 holes matching the holes on the sled base.
The T-track will allow us to use a clamp to SAFELY hold the material we will use to make the WEDGIES
Using a protractor, lay out the WEDGIE and drill the holes in the position needed. The holes should be placed first. Building the WEDGIES and making them accurate is a lot of trial and error, shaving 1000ths off each side, until you can make a perfect ring with all sides touching completely.
Since the sled can also be used to rip and square your material, make a “wedgie” with a 45-degree angle, as shown at right. Since it is not large enough to have a second hole, a small slot is made on the leading edge to accommodate a bolt with a wing nut to lock it down to the sled base.
Woodturners who want to turn segmented objects, need a few more options, and this is what the Wedgie Sled will do best.

This simplified Wedgie Sled improves on the idea, by using the former “setup block” or “wedgie” as a single fence for the workpiece being cut into the desired segments. This also reduces the possibility of error.

Also by reversing the WEDGIE so that the wide end of the “fence” is closest to the blade, the safety of the fence is improved: should the wood get a “catch” on the bottom cut, the wood will move away from the blade instead of into the blade.
Cut a dado on the upper side of the sled to accommodate a piece of T-track. This allows us to use the sled for a tapering sled or simply to straighten an edge on a piece of rough material. This will allow us to cut the tapers for the WEDGIES, as you will see in the video.
After installing the T-track in the dado, make a pass to make the blade side of the sled a zero-clearance edge. This will be the edge you will use to make visual approximations for the adjustments.
After cutting the first WEDGIE to approximate size, cut a set of wedges to test the sled/wedgie for accuracy. Using some scrap material, cut the number of wedges needed to make the complete segment layer.
Lay them out in the circular pattern to see if they make a closed ring. If they fit perfectly the first time, you are incredibly lucky. More than likely, you will have to make some adjustments to the WEDGIE.

If you are making multiple WEDGIES, it’s probably a good idea to label it with the size information.

If you are doing the WEDGIES on a CNC, just include that info into the CNC design.
Notice that there is a “handle” in the CNC version. Why not?? It makes it easier to hold the segment workpiece against the fence. If you don’t have a CNC, a small block of wood can be glued along the back edge of the WEDGIE to serve that function.

The adjustable stop-block in the photo at right can be used to set the length of the segments needed for your segmented piece.

The length of your segments can be calculated in a couple of ways.

Check out the websites on pages which appear later; each has a segment calculator to help you.

Here is another possible design with an adjustable stop [the piece shown in red].

http://www.woodturnersresource.com/extras/projects/segmentcalc/index.html

The website above, has a calculator; you enter the size of your object, and the calculator will produce the information shown below.
For object with multiple layers of increasing or decreasing sizes, you will want to calculate the segment size for all the different layers.

You may treat the bottom as a layer, or simply cut a solid circle of the correct size.

You may use different woods for each layer, or make them all using the same material. Segments may be different woods in a single layer also. Alternating or mixed woods may also be used in the same layer.

Take care that expansion and contraction characteristics of the woods used are not drastically different.
 http://www.quest42.co.uk/woodwork/Segment/Seg-Calc.htm

This is simple to understand.
MAKING A 45-DEGREE FENCE FOR BOXES OR PICTURE FRAMES

The 45° fence is a special case, because if made using both mounting knobs, the top corner of the WEDGIE would extend beyond the top edge of the sled base, thus not supporting the wood. You could make the sled longer, but that’s up to you. I made mine just slightly longer, about 17”.

To avoid this problem, make the WEDGIE with a notch which lines up with the T-track and use a bolt and wing-nut [or a knob] to fix it to the sled when in use.

Links to some videos for WEDGIE SLED VARIATIONS AND IMPROVEMENTS

DEDICATED ADJUSTABLE ACCURATE MITER JIG FOR CUTTING SEGMENTED PROJECT PARTS – 80
https://www.youtube.com/watch?v=e0gfGU-_aJc

        - these spaces before the hyphen were not here when I clicked at end of paragraph
# TABLE SAW SECRETS NOBODY WILL TALK ABOUT FROM THE GOOD OLD DAYS, C&T EPISODE 180
  https://www.youtube.com/watch?v=e8QuLZJM-rU

# QUICK AND EASY WEDGIE SLED
Not so easy as it looks
# https://www.youtube.com/watch?v=nV8Tdmk1xVU

 Dave Gatton MAKES AND SELLS WEDGIES
http://www.davegatton.com/home.html
https://www.youtube.com/user/djgatton

Suggestion:
BUY ONE SET OF WEDGES AND USE A ROUTER TO COPY TO PLYWOOD;
USE THE PLYWOOD VERSION ON YOUR SLED AND REPLACE WHEN IT WEARS OUT!!

# HYBRID WEDGIE SLED
https://www.youtube.com/watch?v=clxeP2UDugQ